## Slide 1: IEC 61499: primer course
Module 3: IEC 61499 standard
Valeriy Vyatkin
Luleå University of Technology and Aalto University

## Slide 2: Plan
What does it define?
Kinds of FBs, common elements: Interface, event, event-data association, data
Basic function block
Composite Function Block
Application / Subapplication
System

## Slide 3: Example of a simple system FLASHER

## Slide 4: Example: FLASHER
Consider a simple product Flashing Lights
Components of the physical system:
PLC (CPU)
START/STOP Button
Mode Selection Switch
  All lights on, count up, count down, chase up and chase down
Time Delay Nub
  Delay between 2 consecutive light flashes
4 LEDs

## Slide 5: FLASHER modelled in software

## Slide 6: FLASHER application
The core functionality is captured in the FLASHER4 FB in a form of state machine

## Slide 7: Model and simulate control logic with IEC 61499
Physical system
IEC 61499 executable model: Runs on PLC or PC (Soft PLC)
HMI
Runs on a computer

## Slide 8: Distributed FLASHER
It is beneficial to model the functionalities in a hardware independent way.
Same block diagram can be executed on different types of controllers or even on a distributed hardware architecture (running on a network of PLCs).

## Slide 9: Motivation: Extensibility

## Slide 10: Distributed deployment

## Slide 11: Extended system

## Slide 12: Common elements

## Slide 13: Parts of IEC 61499 Standard
IEC 61499-1:2012
  Function blocks - Part 1: Architecture
IEC 61499-2:2012
  Function blocks - Part 2: Software tool requirements
IEC TR 61499-3:2004
  Function blocks - Part 3: Tutorial information (withdrawn)
IEC 61499-4:2013
  Function blocks - Part 4: Rules for compliance profiles
Notes: IEC 61499-4:2013 defines rules for the development of compliance profiles, which specify the features of IEC 61499-1 and 61499-2 to be implemented in order to promote the following attributes of IEC 61499-based systems, devices and software tools: - interoperability of devices from multiple suppliers; - portability of software between software tools of multiple suppliers; - and configurability of devices from multiple vendors by software tools of multiple suppliers. This second edition cancels and replaces the first edition published in 2005. It constitutes a technical revision and includes the following significant technical changes: Table B.1 has been updated for consistency with Table 8 of IEC 61499-1:2013.

## Slide 14: Function Block Model: IEC 61131-3
External Interface Specification
IN
BOOL
DB_TIME
TIME
OUT
BOOL
DEBOUNCE
Control Algorithm Specification
DB_FF
S1
R
Q1
OFF_TMR
TON
IN
PT
Q
ET
OUT
DB_TIME
IN
IN
PT
Q
ET
TON
ON_TMR
SR
IN
PT
Q
ET
TON
OFF_TMR
ON_TMR
TON
IN
PT
Q
ET
| |
IN
|/|
IN
(R)
OUT
(S)
OUT
DB_TIME
DB_TIME
Notes: The Function Block in IEC 61499 is an extension to the FB in IEC 61131.
Let’s revise the FB model in IEC 61131 first. In IEC 61131, each FB consists of two parts: an external interface and a control algorithm.
The external interface only contain data signals. The control algorithm can be LD, ST, or a network of other FBs.
In additional to the data interface and control algorithm, events have been introduced to the FBs in IEC 61499.
This slide shows a typical IEC 61131 FB, which has an external interface with some data ports and the corresponding algorithms.
In 61499, FBs are event driven.

## Slide 15: IEC 61131-3 and 61499 Data Types
Signed Integers: SINT(8), INT(16), DINT(32), LINT(64)
Unsigned Integers: USINT(8), UINT(16), UDINT(32), ULINT(64)
Floating Point: REAL(32), LREAL(64)
Bit Strings: BOOL(1), BYTE(8), WORD(16), DWORD(32), LWORD(64) (TRUE, FALSE, 1, 0, 255, 16#FF, etc.)
Character Strings: STRING(8)
Duration: TIME (t#2s, t#1500ms, etc.)
Time: TIME_OF_DAY or TOD DATE DATE_AND_TIME or DT (TOD#17:32:55.678 D#2005-06-07 DT#2005-06-07-17:32:55, etc.)
Derived Data Types: array, enumerated, structured, …
Notes: Identical to IEC 61131-3

## Slide 16: Function Block Type System
Library contains FB type definition
FB types can be instantiated later
Each FB instance can have its own
configuration/setting
Changes in FB types cause automatic changes on all instances
Library of FB Types
FBType
FBInstance1
FBType
FBInstance2
FBType
FBInstance3
FBType
Notes: Once an FB is created, it will be stored in a library as an FB type. These FB types can be instantiated later in the actual design. Each FB instance can have its own configuration but the changes in the FB type will be automatically reflected to all the FB instances.

## Slide 17: Motivation: Intelligent Automation Component
?
Cylinder Software Component
O1
O2
O3
I1
I2
I3

## Slide 18: Communicating components
Cmp1
O1
O2
O3
Cmp2
VAR
a: type1;
b: type2;
c: type3;
L: packet;
…
Cmp3
I1
I1
L.form(Cmp2.I1,a,b);
O1.send(L);
…
L.form(Cmp3.I1,a,c);
O1.send(L);
…

## Slide 19: Message=Event + associated Data
a
b
c
EO1
EO2
k
m
n
EI1
EI2
l
Cmp1
Cmp2
Cmp3

## Slide 20: Events
Event
  Event variables
  Boolean
    0 and 1
  No duration (short duration)
IEC 61499 function block
can only be activated by an event
Event of crossing the line

## Slide 21: Function Block: Header and Body
Upper part of FB is called Header
Lower part of FB is called Body
Notes: Reuse mechanism: Typing – Instantiation

## Slide 22: Function Block of IEC 61499: Interface
Event Inputs
Event Outputs
Data Inputs
Data Outputs
Head
Body
Event – data association: if the event occurs, only the associated data will be updated.

## Slide 23: Function block: Event-Data Association
It is used to transfer data between FBs
Event output “eo” of FB1 is connected by an association line to the event input “ei” of FB2.
Once FB1 emits “eo”, it triggers the execution of FB2.
The values of input parameters “d” and “e” will be updated before the execution starts because they are associated with the event input “ei”.
1- FB1 emits event
4- associated data inputs are sampled to FB2
3- event input is triggered
2- associated data outputs are updated ”on the line”

## Slide 24: Event-data association

## Slide 25: Event-data association
Two instances FB1 and FB2 of the same FB type
  Suppose event FB1.CNF is emitted
  FB1.a is updated and value is sent to FB2.d.
  FB2.d is sampled
  FB1.b is not updated (no association). Therefore FB2.e will not receive the updated value.
Instance Name

## Slide 26: IEC 61499 Function Block Kinds
Basic, Composite, and Service Interface Function Blocks
Execution
Control Chart
Algorithms
Internal
Variables
RSP(+)
SD_1,...,SD_m
Resource
Application
PARAMS
INIT(+)
STATUS
INITO(+)
RD_1,...,RD_n
IND(+)
STATUS
startService
writeOutputs
readInputs
INIT(-)
STATUS
INITO(-)
endService
BFB
CFB
SIFB
Notes: Under the same FB model, there are three different types or classes of FB defined in the standard. The first one is called Basic FB. As the name suggested, Basic FB is the fundamental building block which contains control logics. A Composite FB on the other hand is an encapsulation of FB network. Finally, SIFBs are system dependent FBs use to interface, for example, the hardware I/Os.
I will go through each of them in more detail next.

## Slide 27: XML Exchange Format

## Slide 28: Basic Function Block

## Slide 29: Basic Function Blocks
Execution
Control
Chart (ECC)
Event Input
Data Input
Event Output
Data Output
Algorithms
Algorithms can be programmed in PLC languages
Structured Text
Ladder Logic
etc.
Notes: Basic FB consists of two major parts:
The execution control chart, which is kind of state machine defines the Basic FB’s control logics.
A set of algorithms controls the actual operations.
The execution semantics of Basic FB is as follows:
The execution of a Basic FB starts with the occurrence of an event input;
When an event input arrives, the associated data will be updated;
According to the event and data inputs, the corresponding state in the execution control chart will be activated;
And the related algorithms will be executed. The algorithms can be specified in any language as defined in IEC 61131, such as ST, LD, and so on;
Once the algorithms are completed the newly generated event and data outputs will be issued.
This slide shows a typical IEC 61131 FB, which has an external interface with some data ports and the corresponding algorithms.
In 61499, FBs are event driven.

## Slide 30: Execution Control Chart (ECC)
EC Action
Algorithm
Event
Output
EC
Transitions
Event
Input
Boolean
Condition
EC State
EC State
Initial
EC State
Notes: The most important thing in a Basic FB is the ECC, which is composed by a set of states with the initial state marked by a double square. Except for the initial state, each EC State can associate with a set of EC Actions. Each EC Action can have an Algorithm and the Event Output to be issued after the algorithm’s execution. The EC States are linked via the EC Transitions. The evaluation condition of the EC Transitions can be an event input, a Boolean condition, or a combination of both.

## Slide 31: Transition conditions
Guard
Condition
Event
Input
Boolean
Expression
1
Event input
Boolean expression over data
Event input {&}[Boolean expression over data]
A transition condition can be one of the following:
Examples:
4. REQ [Input_Var=0]
New syntax

## Slide 32: How does Basic Function Block work?
Step 1. The input variable values relevant to input event are made available
Step 2. The input event occurs, the execution control of the FB is triggered.
Step 3. The execution control function evaluates the ECC and notifies the scheduling function to schedule algorithm for execution.
Step 4. Algorithm execution begins.
Step 5. The algorithm completes the assignment of values for the output variables associated with the event output.
Step 6. The resource scheduling function is notified that algorithm execution has ended.
Step 7. The scheduling function invokes the execution control function.
Step 8. The execution control function signals event at the event output.
Notes: The transition conditions are evaluated in the order they are declared in the textual representation of the block (i.e., in XML).

## Slide 33: How does Basic Function Block work?
RES1
RES2
LOGIC
C
B
A
CNF
REQ
INITO
PARAMS
QI
INIT
INT
BOOL
EVENT
BOOL
BOOL
EVENT
BOOL
EVENT
EVENT
BOOL
BOOL
START
REQ&(PARAMS=1)&ACTIVE
1
CNF
INIT
INIT
1
INIT
MAIN
INITO
MAIN
CNF
SHUT
SHUT
REQ & (PARAMS=2)OR(QI=0)
1
ACTIVE:=1
RES1:=0 RES2:=0
QO:=1
] [
] [
]/[
A
B
C
( )
RES1
] [
] [
]/[
A
B
RES1
( )
RES2
ACTIVE:=0
RES1:=0 RES2:=NOT B
QO:=0
1
1
2
0
QO

## Slide 34: Basic FB – execution control chart (ECC)
Basic concepts of fbDA
Each state of ECC can have one or more actions.
An action may have an algorithm call and an output event emission, or both.

## Slide 35: Lifetime of Event Input
EAE stops ECC execution when:
  There are no enabled transition conditions which have not been executed already in this run
  Trick: assign an algorithm, ALG1, to STATE1, within which set INIT:=False. This workaround is not portable.

## Slide 36: Lifetime of Event Input
The first transition with a true condition is executed and the corresponding ECC status of the block is occupied.
The recently used transition is marked so that it cannot be used a second time.
Once there are no transitions to other ECC states left to be fired, because they are already marked and thus executed, or none of the remaining, unmarked transition conditions proves to be true, the markings of the transitions is reset.
FB is waiting for next input event

## Slide 37: Lifetime of Event Input
1
2
3
4
5
6
7
1
2
3
4
5
6
7

## Slide 38: Example: A Basic FB that adds two real numbers

## Slide 39: A Basic FB to add Two Real Numbers

## Slide 40: A Basic FB to Add Two Real Numbers

## Slide 41: Running the basic FB to Add Two Real Numbers

## Slide 42: A Basic FB to Add and Subtract Two Real Numbers
extend

## Slide 43: A Basic FB to Add and Subtract Two Real Numbers

## Slide 44: A Basic FB to Add and Subtract Two Real Numbers

## Slide 45: A Basic FB that Adds and Subtract 2 Real Numbers

## Slide 46: Composite Function Block

## Slide 47: Composite Function Block
  Network of interconnected FBs
  No internal variables
      Latches storing the values of input and output events and data
  Nested composite-in-composite

## Slide 48: Composite Function Block: Example
Computing OUT = X2 – Y2
Interface
Implementation
Event
Data

## Slide 49: Hierarchical composition

## Slide 50: Composite Function Block
Execution Control:
  No ECC
  No internal variables
To ensure a particular order of execution, user can implement a supervisor basic function block

## Slide 51: Rules for event connections
  Event split is equivalent to using E_SPLIT standard library FB
Basic concepts of fbDA
=

## Slide 52: Event merge
  Event merge is equivalent to using E_MERGE standard library FB
Basic concepts of fbDA
=

## Slide 53: Data connections
  Data connections – cannot be merged, but data split is allowed.
Basic concepts of fbDA

## Slide 54: Service Interface Function Block

## Slide 55: Service interface function blocks (SIFB)
  Mechanisms for interacting with hardware resources
  PC and different vendor printers – need drivers to command printer to print and get status information
  Similar with SIFB – to get data from sensors and PLCs, and control actuators
  SIFB implementation requires low level knowledge of particular hardware
  Provided by vendor
  Encapsulation of IP
HP, DELL, EPSON, CANON, XEROX, Konika Minolta, RICOH
drivers

## Slide 56: Service Interface Function Blocks (SIFB)
Modelled as sequences of service primitives per ISO TR 8509
Notes: Binary code

## Slide 57: Operations with events

## Slide 58: Process interface: read inputs and write outputs

## Slide 59: Elements of Distributed systems

## Slide 60: Resource Model
The main execution container of FB network
Each Resource is independent of other Resources in the device
Access to Communication and Process interfaces via SIFBs
Responsible for the scheduling of FBs
Process interface(s)
Communication interface(s)
SFB
SFB
FB Network
Scheduling Function
Communication mapping
Process
mapping
Notes: Above the FB model is the Resource Model, which contains an FB network and provides it the access to communication and process interface via SIFBs. Each Resource also comes with a Scheduling Function to schedule the execution FBs inside the FB network.

## Slide 61: Resources – scheduling functions
Schedule algorithms for execution
Determines sequence
  Of FBs execution
  Of algorithms execution

## Slide 62: Device Model
An abstract model represents a physical instrument interacting with automation systems or process information, e.g.
  PLC, CNC, microcontroller, etc.
Notes: Resources are further contained in Devices, which represent physical instruments such as a computer or a microcontroller and etc. Each device can contain multiple Resources and all Resources use the same communication and Process interfaces of the Device.
Process interface is the mapping between the physical entities (sensors, actuators) and the resource

## Slide 63: Device Model
A Device is specified by it process interfaces and communication interfaces
  Process interface is the mapping between the physical entities (sensors, actuators) and the Resource
Contains multiple Resources
All Resources use the same Communication and Process interfaces of the Device
Resource 1
Resource 2
Resource 3
Process interface(s)
Communication interface(s)
Application A
Application B
Application C
Notes: Resources are further contained in Devices, which represent physical instruments such as a computer or a microcontroller and etc. Each device can contain multiple Resources and all Resources use the same communication and Process interfaces of the Device.
Process interface is the mapping between the physical entities (sensors, actuators) and the resource

## Slide 64: Device model: example of use

## Slide 65: Device classes
  Class 1
  New instance of FB library
  Class 0:
    Preprogrammed FB instances
    FBs connections can be changed
Class 2
Fully reprogrammable
Can create FB types

## Slide 66: Device type definition
  Interface of the device may have only data inputs.
  Example: SE.DPAC.M251_dPAC
    Deployment IP Address:Port
    HMI IP Address:Port
    Watch IP Address:Port
    Archive Service IP Address:Port

## Slide 67: Resource type definition
  EMB_RES_ECO, PANEL_RESOURCE, VIEW_RES
    Default function block START of E_RESTART

## Slide 68: Device management
  By default, devices contain resource MGR
  KERNEL of TYPE DM_KRNL
    Executes received management commands
    Configuration tool manages the device

## Slide 69: Device management
  Dev_MGR receives commands in XML
  Replies back with confirmation or errors

## Slide 70: Device management
  Dev_MGR receives commands in XML
  Replies back with confirmation or errors

## Slide 71: Application
Application is a design artefact
Consists of a network of FBs
Designed independently from hardware where it will be deployed to
Deployment: mapped to one or several devices
Notes: Applications are design artifacts which consists an FB network contains the entire design. Applications are designed independent from hardware and can be mapped totally or partially across different Devices.

## Slide 72: Application: Example

## Slide 73: Subapplication
Type definition, like for function blocks
Interface, but without event-data associations
Defined by a function block network, like Composite FB
No latching of events and data,
direct propagation

## Slide 74: System Configuration
Represents the physical deployment of the design
Consists of:
  Communication network
  Devices
  Controlled process and machines
Device 2
Device 3
Device 4
Device 1
Application A
Appl. C
Application B
Controlled process/machines
Communication network
Notes: The top-level model in IEC 61499 is call System, which represents the physical deployment of the design and consists of communication network, devices, and the controlled process and machines. As you can see from this diagram, there are three entities called Applications in the System.

## Slide 75: Distribution of Application
Event flow
Data flow
Application =
Function Block Network
Device 2
Communication network
Device 3
Device 4
Device 1
Application A
Appl. C
Application B
Controlled process/machines
System = Communication Network + Devices +
Process/Machines
Application can be deployed to several devices
A device in the system can contain and execute parts of different applications
Notes: For instance, Application A is mapped to three Devices in this System.

## Slide 76: Distribution of Application
Tools usually insert the communication blocks automatically
Notes: Communication between devices
Tools usually insert the communication blocks automatically
Or one can insert them manually using the PUBLISH and SUBSCRIBE function block types included as part of the standard library

## Slide 77: Example: Distributed systems configuration

## Slide 78: Example: Distributed systems configuration

## Slide 79: Composite Automation Type (CAT)

## Slide 80: Composite Automation Type (CAT)
Object-oriented mechanism of creating visualisation for automation projects
  Object-oriented
  Self-contained
  Reconfigurable
Each CAT consists of:
  Visualization symbols
  Control logic
  Plant models
  HMI and I/O connections
Supports:
  Direct hardware interaction
  Automatic deployment of control logic
Notes: FBs can be designed following many patterns. One popular pattern is called CAT, which follows the well-known MVC design pattern from software engineering.
Each CAT consists of …
You have learned design patterns for PLCs.
You will also learn design patterns for distributed systems.

## Slide 81: CAT
Software representation of real instruments/devices, e.g. pump
Predefined control structure with abstract hardware interface
Automatic HMI configuration and connection

## Slide 82: System architecture with an implicit HMI device

## Slide 83: Application with CATs

## Slide 84: Model of Composite Cylinder

## Slide 85: CAT creation

## Slide 86: How does a CAT work?

## Slide 87: Normal establishment

## Slide 88: Normal operation

## Slide 89: Normal termination

## Slide 90: Operation is inhibited

## Slide 91: Event-handling Function Blocks

## Slide 92: Count UP
BOOL
UINT
UINT
Action
Output event
Algorithm

## Slide 93: Count down
BOOL
UINT
UINT

## Slide 94: Count UP/Down
BOOL
UINT
UINT
BOOL

## Slide 95: E_CYCLE
TIME

## Slide 96: Data latch
BOOL
BOOL
CLK
D
EO
Q

## Slide 97: Event switch E_SWITCH
BOOL
EI
G
EO0
EO1

## Slide 98: Event demultiplexor
UINT

## Slide 99: Boolean falling edge detection
BOOL
EI
QI
EO

## Slide 100: Boolean raising edge detection
BOOL
EI
QI
EO

## Slide 101: E_MERGE

## Slide 102: Train of events

## Slide 103: E_TABLE_CTRL
UINT
TIME[4]
In this example N<=4
TIME
UINT

## Slide 104: Table-driven sequence of events
UINT
TIME[4]
UINT

## Slide 105: Controlled Event propagation E_PERMIT
BOOL

## Slide 107: RS, SR triggers
BOOL
BOOL

## Slide 108: Event selector
BOOL

## Slide 109: Event splitter

## Slide 110: Event driven toggle of a Boolean output
BOOL